## Slide 1: An overview of Energy Storage Technologies - II
Abdulnaser Sayma
Professor of Energy Engineering

## Slide 2: Consent
Electrical Energy storage
Efficiencies – the technical staff
Various definitions
Characterisation of energy storage technologies
The most common energy storage technologies
Conclusions

## Slide 3: Electrical Energy Storage
We concluded that we need to install excess renewable capacity and store some energy for use when demand is higher than capacity or when renewable systems are not producing
Electrical Power generation
Solar, wind, other
Storage medium or devise
Consumption
Domestic, industrial, other
Direct consumption
Excess – converted to storable form
Convert to electricity

## Slide 4: Efficiency
We are used to the usual definition of efficiency of energy conversion device as: Electrical energy output over primary energy input:
When you convert electrical energy to a form that can be stored, you lose some energy, so we need to define conversion efficiency.
When we convert stored energy to electricity we lose some more, so there is another efficiency of conversion
The round-trip efficiency (RTE) is the multiplication of the two efficiencies.
The higher the round-trip efficiency, the better the system

## Slide 5: Various Definitions
Energy Storage can be grid scale (at Point Of Generation – POG - or distributed) or behind-the-meter
POG grid scale requires larger grid for equal effect
Behind-the-meter can support higher costs
Storage technologies are currently too expensive to support transition to net-zero

## Slide 6: Energy Storage Characterization
There are two key factors that characterise energy storage:
Capacity - the rate at which energy can be delivered from storage (kW), or multiples
Duration - the length of time it can sustain that rate of output, which is determined by the amount of energy stored (kWh) or multiples

## Slide 7: Important energy storage metrics
Cost per kW
Cost per kWh
Round Trip Efficiency (RTE)
Longevity
Grid scale or “behind the meter?”
Environmental impact

## Slide 8: Types of Primary Energy Storage
Thermal: hot water, hot salts, ice
Electrical, fully bi-directional
Direct electrical storage: capacitor or superconducting coil
Electrochemical : battery (including flow type)
Mechanical : Hydro potential, compressed air, flywheel
Chemical : fuels such as petrol, diesel, gas, hydrogen
Can be bi-directional with fuel cell but efficiency is low More typically make using
excess renewable power and burn when demand is high/generation low

## Slide 9: Electrochemical : Battery
Energy stored chemically
Electrical power released by reaction
Common chemistries Lead-Acid and Li-Ion
Source: http://www.wholesale-electrical-electronics.com/p- solar-battery-np12-200ah-12v-200ah-855419.html

## Slide 10: Super Capacitors
Relay on charge build up between plates with an air gap when voltage is applied
Charge can be increased by using dielectric material between the plates
Electrolytic capacitors include rough oxide as dielectric material which increases surface area and hence charge stored.

## Slide 11: Superconducting magnetics storage
Stored energy in a magnetic field when a current flows around a coil.
The coil is made of superconducting material so that there is no resistance energy loss
Superconducting material is expensive and must be cooled cryogenically.
Offers the highest round trip efficiency

## Slide 12: Mechanical : Compressed/Liquid Air
Energy stored in compressed air or other gas
Uses motor driven compressor to compress gas
Energy released in the turbine generator
Many variants particularly how heat is treated
Source: http://highview- power.com/technology/
16
Source: http://www.climateandfuel.com/pages/storage.htm

## Slide 13: Mechanical : Pumped Hydro
Electricity generated in a turbine generator
Energy stored by pumping water back by reversing the turbine to act as a pump
Source: http://www.bbc.co.uk/scotland/learning/bitesize/ standard/physics/energymatters/generation_of_electricity_rev3.shtml

## Slide 14: Mechanical : Flywheel
Electricity stored in the kinetic energy of a rotor and converted using a motor-generator
Source: http://www.acsystems.co m/vycon/
14

## Slide 15: Power and discharge times

## Slide 16: Main points covered
The need for electricity storage in a renewables dominated system
Efficiencies and other definitions – RTE
Characterisation of energy storage technologies
Overview of the most common energy storage technologies
Comparison of some of the key technologies