## Slide 1: Pumped Hydro Energy Storage
Abdulnaser Sayma
Professor of Energy Engineering

## Slide 2: Consent
Hydro power
Calculations of waterpower
Solving intermittency
Hydro turbines technology and turbine selection
Typical pumped hydro installation
Worked example
Conclusions

## Slide 3: Hydro power
Origin: solar power
¼ of incident solar energy consumed in evaporation
Only 0.06% of that is retained by precipitation as a potential hydropower resource.

## Slide 4
Requires a suitable location to build dam and store water behind.
Typically in the order of GW
Typically in the order of KW.
Avoids environmental issues and costs associated with dams
Dam
Run of the river

## Slide 5: Water Power
Power output depends on hQ. So, for a given power output you need either h with small Q or Large Q with low h
Typical units: MW-hours or multiples.

## Slide 6: Turbines types
Reaction Turbines
  Derive power from pressure drop across turbines
  Totally immersed in water
  Angular motion converted to shaft power
  Propeller, Francis and Kaplan
Impulse Turbines
  Convert Kinetic energy of water jet hitting buckets
  No pressure drop across turbine
  Pelton, Turgo and cross flow turbines

## Slide 7: Reaction turbines
Kaplan
Francis
Propeller

## Slide 8: Impulse turbines
Pelton Wheel
Turgo
Cross flow

## Slide 9: Turbine selection chart

## Slide 10: Pumped Hydro Energy Storage
Electricity generated in a turbine generator
Energy stored by pumping water back by reversing the turbine to act as a pump
Source: http://www.bbc.co.uk/scotland/learning/bitesize/ standard/physics/energymatters/generation_of_electricity_rev3.shtml
It is also possible to use the sea as the lower reservoir. However, Turbine materials need to resist corrosion by sea water

## Slide 11: Worked example
A wind farm is delivering 50 MW average excess power over a period of 24 hours that is required to be stored in a pumped storge plant with upper and lower reservoir height difference of 600 m. The pump efficiency is 95%,
The amount of excess electrical energy in this period
calculate the volume of water that raised to the upper reservoir
Calculate the electrical energy supplied if this water is released to a turbine of efficiency 90%
(a) Excess Electrical Energy
(b) Volume of water
Given
Re-arrange
Volume = Volumetric flow rate X Time
(c) Electrical Energy supplied: E

## Slide 12: Undersea pumped hydro Energy Storage
The concept is to put a strong container deep under the sea, connected to the surface through a pipe and filling with water drives a turbine to generate electricity.
When excess energy is available, water is pumped out to the the surface, storing electrical energy while evacuating the container
Saves the need for a second reservoir, but challenges with installing high pressure vessel under sea
Sea water surface
Pump out using excess electricity
Sea water surface
Fill generating electricity
Charge
discharge

## Slide 13: Advantages of Hydropower
Rapid response to changing demand
Can store large amounts of energy
Can be used for short, medium and long term storage
Round-Trip Efficiency exceeds 85%
Releases no CO2 and negligible oxides of Sulphur and nitrogen
No particulate matter, does not emit radioactivity
Does not cause major fires

## Slide 14: Drawbacks
Displacement of population and wild life
High cost of the infrastructure – very long payback periods.
Danger of dam failures and flooding
Water pollution
Could produce methane due to decaying organic matter under the lake – 30 times more potent than carbon dioxide for greenhouse effect.

## Slide 15: Conclusions
Pumped hydro is can make use of the well-established hydroelectric power for grid scale electrical energy storage.
Its main advantages is the rapid response to storage and demand
Limitations arise from the need for suitable geographical locations
Draw backs are similar to large hydro schemes, primarily the high initial investment costs and other associated environmental and social impacts