## Slide 1: Environmental factors of energy storage
Abdulnaser Sayma
Professor of Energy Engineering

## Slide 2: Consents
Introduction
Technology Specific Environmental Impact
Conclusions

## Slide 3: Introduction
Due to the wide range of available electrical energy storage technologies, it is usually not suitable to discuss their environmental impact collectively, however,
Environmental impact depends on the nature of the technology. Things to consider:
  Impact of construction work associated with the system
  Materials used and their impact – mining, energy utilization during manufacture etc.
  Toxic materials or CO2 emissions that may be released during operation
If the source of energy is renewables, then storage can be considered sustainable and emissions free
Environmental benefits, in that case are, in general, similar, leading to overall reduction in CO2 emissions, enhanced grid stability and reduced cost of electrical energy
If the source of energy stored is fossil fuels, then associated environmental implications of the energy source should be accounted for.

## Slide 4: Technology-Specific Environmental considerations

## Slide 5: Pumped storage hydro
Positives
Rapid response to changing demand
Can store large amounts of energy
Can be used for short, medium- and long-term storage
High round-Trip Efficiency exceeds 85%
Environmental concerns
Significant disruption during construction
Displacement of population and wildlife
High cost of the infrastructure – very long payback periods.
Danger of dam failures and flooding
Water pollution
Could produce methane due to decaying organic matter under the lake – 30 times more potent than carbon dioxide for greenhouse effect.

## Slide 6: Compressed Air Storage
If the plant is charged using renewable resources, then environmental impact is minimal and is typically associated with the construction phase, but this is similar to the impact of installing a standard gas turbine power plant with limited impact when compared to schemes like pumped hydro.
The other main consideration is the compressed air store. For large plants where this is typically an underground cavern, there should be an assessment of potential ground movement, but this is mostly not a significant issue

## Slide 7: Battery Storage plants
The main environmental issue is associated with the mining and processing of the materials used in batteries. These are typically hazardous materials.
For example, Cadmium can affect animals and humans if ingested and if it enters the body, it remains there for a long time
Lithium, which is used in lithium-ion and lithium hydride batteries, is extremely reactive when exposed to air
Lithium batteries are also capable of catastrophic failure and safety circuits are required to ensure that their operating conditions are carefully controlled
Sodium sulfur batteries are also potentially hazardous due to the presence of liquid sodium
There has been some incidents with batteries exploding.
Lead, common in lead-acid batteries, can be hazardous if not managed carefully
A plant designed solely for energy storage will have no further impact when it is operating if maintained correctly and is carefully disposed or recycled at the end of life.

## Slide 8: Superconducting magnetic energy storage
It relies on a coil made from metal alloys or special ceramics that must be cooled to extremely low temperatures in order to function.
The low-temperature refrigeration system can be hazardous if not managed carefully.
It creates a very powerful magnetic field that must be carefully shielded.
The magnetic field also puts elements of the structure under great stress so components must be engineered to withstand these forces.
However, there are no major environmental issues associated with this technology that would not be associated with other electrical, magnetic, and low-temperature systems

## Slide 9: Flywheels
Flywheel energy systems are relatively small, mechanical-based energy storage devices. They contain motors and generators as well as the flywheel itself.
All these elements will generate some noise but this can be limited with good sound insulation.
The main hazard is that of catastrophic failure of the flywheel itself due to the large centrifugal forces.
To counter this flywheel systems must be housed in massive enclosures that can contain the parts of the device rotating at high speed

## Slide 10: Super-capacitors
A super-capacitor is a relatively compact, small-scale energy storage system based on advanced electrochemical technologies.
The device can store a large amount of electrical charge in a relatively small space, and if this is discharged quickly it has the potential to cause significant damage, both externally and internally.
Super-capacitors materials are relatively standard and mostly not hazardous
There are arguments that supercapacitors are preferable to the more common lithium-ion batteries because of environmental issues with the latter, suggesting that these devices are considered environmentally benign.

## Slide 11: Hydrogen Energy Storage
The use of hydrogen as an energy storage medium involves three stages, hydrogen production, hydrogen storage and hydrogen use.
Production using surplus electrical power is a simple and straightforward process with few hazards except those associated with the product gases themselves, hydrogen and oxygen.
The challenges associated with storage are greater, similar to those associated with natural gas with the exception that accidental release of hydrogen into the atmosphere, provided it dissipated quickly, has no significant environmental impact.
There is no danger to humans or animals from contact with the gas. However, it is explosive, so care has to be taken that it does not build up in enclosed spaces.
When hydrogen is to be used to generate electric power, this will be by reaction with oxygen, either in a combustion plant or in a fuel cell. In both cases the oxygen will normally come from air and the reaction product will be water, usually in gaseous form which is considered environmentally benign.

## Slide 12: Conclusions
There are specific environmental issues associated with electrical energy storage systems
These are mostly associated with the disruption during construction and or the materials used
Other issues related to health and safety of operation and noise in some cases. These are known solutions to these issues
The overall benefit or reduction in cost of electricity and reduction in CO2 emissions associated with energy storage mostly outweigh any environmental consideration