## Slide 1: Solar PV
Dr Tala El Samad
March 2024

## Slide 2: Content
    Introduction to Solar Energy
    PV Technology
    PV Modules
    Current Status & Future Potential

## Slide 3: The Solar Energy Cycle
Total solar energy received by earth ~ 109 TWh
Total energy consumed ~ 105 TWh
3

## Slide 4: Solar Energy Variation
Solar energy is variable:
  Wavelength
  Direct and diffuse radiation
  Sun-Earth geometry
  Tilt and orientation
4

## Slide 5: Estimating Availability
Easy to predict:
  Sunpath
  Hours of sunlight/ intensity
Cloud cover biggest source of variability
Predict based on statistical data
Sunshine hours (insolation)
  Measured
  Estimated
Proportion of beam radiation (which is focusable on plate)
Effect of inclination (how much of diffuse radiation is collected)
Temperature also important
5
Sunny day
Cloudy day
Faranda, Roberto, and Sonia Leva. "Energy comparison of MPPT techniques for PV Systems." WSEAS transactions on power systems 3.6 (2008): 446-455.

## Slide 6: Solar Energy
Electricity generation
Solar heating and cooling
Photovoltaics (PV)
Solar thermal
6

## Slide 7: Timeline
Mid- nineteenth century:
Basis & proof of concept
1960s:
PV device development for space programmes
- upwards of
$250,000/kWe
1970s:
replacing non rechargeable batteries + small scale power generation
2003:
over 700
e
MW of
solar cells at
$2,500/kWe
2010:
continuous growth
$1,000/kWe
Onwards
7

## Slide 8: Where are PVs used?
< 10 kWe for residential buildings
Up to 100 kWe in both residential and commercial properties
Up to 1 MWe for commercial applications
Few installations up to 10 MWe
Usually anything above, CSP is installed for power generation
Some large solar farms up to 1000s of MW but require large space
8

## Slide 9: Why PVs?
Simple components
No moving parts
Noise-free
Modular/ scalable for applications ranging from Watts to MegaWatts
Direct integration into unit producing power for
Potentially low maintenance costs
9

## Slide 10: A Simple PV System
Solar PV converts solar energy directly into electricity
Solar cell is the simple building block
Solar panel consists of multiple cells
Solar array consists of multiple panels
Control panel
Inverter converts from DC to AC power
Stand-alone or grid connected
Cell
Panel
Array
CONTROL PANEL
INVERTER
END-USER
ELECTRIC GRID
10

## Slide 11: The Photoelectric Effect
The photovoltaic effect is the generation of current or voltage in a material upon exposure to light
Direct conversion from light to electricity with no moving parts
Discovered by Edmond Becquerel in 1839
11

## Slide 12
Semiconductors
Electron partially immobilised
Hole Locally positively charged
Allows electrons to move freely
12

## Slide 13: Generating Current
Photon strikes a conductive material
Material’s electrons can capture the energy
If enough energy, electrons are excited
The electron must be withdrawn before it relaxes
Creation of voltage difference directs migration of electron to produce current
13

## Slide 14: Solar PV Types
PV collectors fall into Flat Plates vs Concentrators
  Concentrators:
    employ lower cost mirrors or lenses to focus energy on smaller area which leads to increased performance and lower costs
    downfall is utilizing only direct/ unscattered portion of solar spectrum making flat-plates more versatile
  Flat plates are far more common — utilizing solar cell material over entire exposed area
Module constitute 50–60% of total capital cost (inverters, control/storage…)
14

## Slide 15: Solar PV Performance
Collector area to meet load decreases in direct proportion to increased efficiency
Measures of efficiency: lab-scale experimental, prototype modules, field- deployed modules) around 20 – 30% depending on measure
15

## Slide 16: Mono vs Poly crystalline Si Cells
High manufacturing cost
oExpensive crystal growth
process
oHighly skilled operators
oElectronic grade silicon
High efficiency (2 ‒ 3% higher than poly)
Made from a single silicon crystal
Cheaper to manufacture
oMolten polycrystalline silicone cast
into ingots
oCan be formed into square so no gaps between cells
Less efficient than monocrystalline cells
16
Composed of multiple crystals

## Slide 17: Solar Cells
Amorphous Silicon
Non-crystalline structure (random structure)
Low efficiency (5 – 10%)
Low cost
Trade-off between performance and cost
More coverage for same power output
Better reaction to diffused light
Relatively low lifespan
17

## Slide 18: Thin-Film Solar Cells
Copper Indium Galium Selenium (CIGS)
~20% efficiency for lab cell
~16% for mini-module @ 20cm2
Most efficient thin-film
Wide band gap covering most of the visible spectrum
R&D challenges to depose films in clean, high-vacuum environment
Associated environmental damage with mining and refinement
Cadmium Telluride (CdTe)
Cheap electroplating-type manufacturing process
Band gap 1.44 eV close to optimum for solar spectrum
16% laboratory efficiency and no performance degradation
Cadmium highly toxic
18

## Slide 19: Laboratory Solar Cells
Multi-junction solar cells
Multiple solar junctions
Different band gap
Each junction designed to absorb a particular part spectrum
High efficiency, in excess of 40% in lab
Very high cost
Specialised applications
19

## Slide 20: Laboratory Solar Cells
Organic solar cells
Growing field of study
Use organic (carbon-based) molecules
Organic molecules can be processed quickly leading to large volume,
low cost production
Good flexibility and tuning of the band-gap
But …
Low efficiency, Low stability, Low strength
Not yet commercialised widely
20

## Slide 21: Performance Limits
Technology | Efficiency | Lifespan | Main uses
Single crystal Silicon | 12 – 25% | 30 years | Space, roof modules, facades etc.
Polycrystalline Silicon | 11 –15% | 30 years | Roof modules, facades, generators, farms on ground etc.
Amorphous | 5 –10% | 10 years | Electronics (watches, calculators), integration with buildings
CIS | 9 –11% | > 20 years | Integration in buildings
Multi-junctions | Up to 45% |  | Space
CdTe | 6 – 10% | > 20 years | Electronics (watches, calculators), integration in buildings
CIGS | Up to 20% | - | Space, integration in buildings
Organic | 6 – 15% (Lab) | > 10 years | Under development
21

## Slide 22: Performance Limits
22
https://www.nrel.gov/pv/assets/pdfs/best-research-cell-efficiencies-rev220630.pdf

## Slide 23: Performance Limits
Loss of energy above band gap/ Limiting band-gap energies at low energy levels
Reflective losses on surface
Loss of effective interception area
Ineffectiveness of photon-electron interactions
Resistance losses in the circuit
Recombination of electrons and holes outside p-n junction
23

## Slide 24: Feed-In Tariff (FIT)
Energy Source | Scale | FIT (p/kWh) |  |  | Duration (years)
 |  | Low | Middle | High | 
Solar PV | ≤10 kW | 0.15 | 3.49 | 3.87 | 20
Solar PV | 10 – 50 kW | 0.15 | 3.71 | 4.12 | 20
Solar PV | 50 – 250 kW | 0.15 | 1.55 | 1.73 | 20
Solar PV | 250 – 1 MW | 1.36 |  |  | 20
Solar PV | 1 – 5 MW | 0.15 |  |  | 20
Solar PV | Standalone (< 5 MW) | 0.05 |  |  | 20
https://www.ofgem.gov.uk/environmental-programmes/fit/fit-tariff-rates
Government scheme of payment for generating own electricity which can be sold back to the grid
To promote uptake of small-scale, renewable, low-carbon electricity generation technologies
24

## Slide 25: Future Potential of Solar PV
https://www.irena.org/-/media/Files/IRENA/Agency/Publication/2019/Nov/IRENA_Future_of_Solar_PV_2019.pdf
25

## Slide 26: Economics
https://irena.org/-/media/Files/IRENA/Agency/Publication/2019/Nov/IRENA_Future_of_Solar_PV_2019.pdf
26
Plummeting costs

## Slide 27: 0–4 kW PV Installations in UK
27
https://www.gov.uk/government/statistics/solar-pv-cost-data

## Slide 28: 0–4 kW PV Mean cost per kW in UK
https://www.gov.uk/government/statistics/solar-pv-cost-data
28

## Slide 29: Environmental Impact
http://www.nrel.gov/docs/fy13osti/56487.pdf
http://www.nrel.gov/docs/fy04osti/35489.pdf
29

## Slide 30: End of presentation
School of Science & Technology
City, University of London
Northampton Square
London
EC1V 0HB
United Kingdom
T: +44 (0)20 7040 5060
E: department@city.ac.uk
www.city.ac.uk/department