## Slide 1: Renewable Vs. conventional energy sources
Prof. Abdulnaser Sayma

## Slide 2: Contents
The context
Sources of energy
Power generation fuels
Energy conversion systems
  Conventional
  Renewable
Back up to intermittent renewables
Concluding remarks

## Slide 3: The context
Primary energy demand and projected growth
Renewables growth – share
We will see that both are important in the short, medium and mostly long term and thus studying underlying technologies are necessary

## Slide 4: Energy resources

## Slide 5: Sources of primary energy
Chemical
  Fossil Fuels (Solar!)
  Biofuels (Solar!)
  Nuclear!
Solar
  Direct insolation
  Wind
  Wave
  Hydro
Geothermal
Tidal

## Slide 6: Power Generation
Thermal:
Fossil Fuels
Biofuels
Nuclear
Geothermal
Concentrated Solar
Mechanical
Wind
Tidal
Hydro
Engine:
Reciprocating
Rankine – turbine
Gas turbine
Shaft Power
Turbine:
Electricity
Generator
Electrochemical
(fuel cell)
Hydrogen
Methane
Solar
Photovoltaic cell

## Slide 7: Conventional power generation - I
Spark and compression-ignition engine
Steam or organic Rankine power plant
Combustion Gas turbine power plant
Combined cycle power plant
Nuclear power station
Hydroelectric power station
Thermo-chemical

## Slide 8: Conventional power generation - II
In all cases, a prime mover is used to provide shaft power which is in turn used to drive a generator.
In cars shaft power is used to provide traction
Also, may be used to drive a gas compressor or drilling equipment for example

## Slide 9: Coal fired power plants

## Slide 10: Nuclear power plants

## Slide 11: Reciprocating engines

## Slide 12: Gas Turbine power plants

## Slide 13: Industrial gas turbines
Siemens 94A
300 MW F class
Notes: Single shaft
15 stage axial compressor
4 stage axial turbine
Annular combustor with 24 burners
Thermal efficiency approaching 40%

## Slide 14: Aeroderivatives
GE: LM2500

## Slide 15: Simple Gas turbine system
Air
compressor
turbine
Heat Addition
Power output
Notes: For an ideal compressor and Turbine, if fuel is not burned in the combustion chamber, the turbine power will be just sufficient to drive the compressor.
However, because of irreversibility (Component losses), turbine power will not be sufficient to drive the compressor.
If fuel is burned in the combustion chamber, the turbine power will be in excess of driving the compressor and additional power output is produced.
The specific power output is related to turbine inlet temperature which is limited by turbine material life
Thermal efficiency is a function of pressure ratio which primarily depends on compressor design

## Slide 16: Regenerative cycle
Air
Fuel
compressor
turbine
Combustion
Heat Exchanger
Exhaust
Notes: In the regenerative cycle, the hot gases exiting the turbine are used to preheat the compressed air before entering the combustion chamber thus reducing the fuel burned to reach the required turbine inlet temperature.
However, the pressure ratio should not be high such that the compressor exit temperatures approaches or exceeds the temperature of the turbine exhaust gases.
Also the additional cost and weight of the heat exchanger needs to be taken into account. In fact, for jet propulsion application, the additional efficiency gain should be balanced by the combination of reduced fuel consumption and hence the weight of the fuel carried on board together with the weight of the heat exchanger. Also the fact that the heat exchanger is bulky and needs to be place in such away that the engine size and hence related drag are not significantly increased. It turns out the the regenerative cycle has not been used in any in service aircraft engine even though there were some attempts to develop and test a turboshaft regenerative engine by Allison.

## Slide 17: Combined Cycle
GENERATOR
Air
Fuel
compressor
turbine
Combustion
GENERATOR
Steam
turbine
boiler
steam
Exhaust gases
condenser
pump

## Slide 18: Microturbines – Combined heat and power
Notes: Typically below 1MW, but nowadays, they exist in the range of 10s of kW
Used for CHP applications

## Slide 19: Power Generation from Gas

## Slide 20: Renewable power generation

## Slide 22: Solar thermal

## Slide 23: Wind power

## Slide 24: Hydroelectric

## Slide 25: Wave power

## Slide 26: Tidal power
Earth
moon
Sun
Sun
Earth
moon
Neap tide
spring tide
Solar tide
Lunar tide

## Slide 27: Geothermal

## Slide 28: Back up power for renewables
Most of the renewable power in the grid is solar or wind
These are intermittent resources
There is a need for standby conventional power to provide back up power at night or when wind does not blow
There is not enough storage capacity or sufficient interconnections to provide the back up

## Slide 29: Back up power
Most backup power is provided by GT or CCGT power plants
Some is provided by coal power plants
This has implications on the cost of electricity from these plants:
  They do not provide their full capacity
  Frequent starts, shut downs and ramping up and down affect life of components
Running at off-design conditions increases emission levels

## Slide 30: End of presentation
School of Science & Technology
City, University of London
Northampton Square
London
EC1V 0HB
United Kingdom
T: +44 (0)20 7040 8277
E: a.sayma@city.ac.uk